## Slide 1: CS 179: GPU Computing
Lecture 2: The Basics
Notes: Resume – remarks:
Welcome back
Storytelling/motivational purposes
Introducing

## Slide 2: Recap
Can use GPU to solve highly parallelizable problems
  Performance benefits vs. CPU
Straightforward extension to C language

## Slide 3: Disclaimer
Goal for Week 1:
  Fast-paced introduction
  “Know enough to be dangerous”
We will fill in details later!

## Slide 4: Our original problem…
Add two arrays
  A[] + B[] -> C[]
Goal: Understand what’s going on

## Slide 5: CUDA code (first part)

## Slide 6: Basic “formula”
Setup inputs on the host (CPU-accessible memory)
Allocate memory for inputs on the GPU
Copy inputs from host to GPU
Allocate memory for outputs on the host
Allocate memory for outputs on the GPU
Start GPU kernel
Copy output from GPU to host

## Slide 8: “Classic” Memory Hierarchy

## Slide 9: The GPU

## Slide 10: The GPU
“Global memory”

## Slide 12: Pointers
Difference between CPU and GPU pointers?

## Slide 13: Pointers
Difference between CPU and GPU pointers?
  None – pointers are just addresses!

## Slide 14: Pointers
Difference between CPU and GPU pointers?
  None – pointers are just addresses!
  Up to the programmer to keep track!

## Slide 15: Pointers
Good practice:
  Special naming conventions, e.g. “dev_” prefix

## Slide 18: Memory allocational
With the CPU (host memory)…
  float *c = malloc(N * sizeof(float));
  Attempts to allocate #bytes in argument

## Slide 19: Memory allocation
On the GPU (global memory):
  float *dev_c;
  cudaMalloc(&dev_c, N * sizeof(float));
Signature:
cudaError_t cudaMalloc (void ** devPtr, size_t size)
  Attempts to allocate #bytes in arg2
  arg1 is the pointer to the pointer in GPU memory!
    Passed into function for modification
    Result after successful call: Memory allocated in location given by dev_c on GPU
  Return value is error code, can be checked

## Slide 22: Memory copying
With the CPU (host memory)…
  // pointers source,destination to memory regions
  memcpy(destination, source, N);
Signature:
  void * memcpy (void * destination, const void * source, size_t num);
  Copies num bytes from (area pointed to by) source to (area pointed to by) destination

## Slide 23: Memory copying
Versatile cudaMemcpy() equivalent
  CPU -> GPU
  GPU -> CPU
  GPU -> GPU
  CPU -> CPU

## Slide 24: Memory copying
Signature:
  cudaError_t cudaMemcpy(void *destination, void *src, size_t count,
  enum cudaMemcpyKind kind)
f

## Slide 25: Memory copying
Signature:
  cudaError_t cudaMemcpy(void *destination, void *src, size_t count,
  enum cudaMemcpyKind kind)
Values:
  cudaMemcpyHostToHost
  cudaMemcpyHostToDevice
  cudaMemcpyDeviceToHost
  cudaMemcpyDeviceToDevice
F

## Slide 26: Memory copying
Signature:
  cudaError_t cudaMemcpy(void *destination, void *src, size_t count,
  enum cudaMemcpyKind kind)
Values:
  cudaMemcpyHostToHost
  cudaMemcpyHostToDevice
  cudaMemcpyDeviceToHost
  cudaMemcpyDeviceToDevice
F
Determines treatment of dst. and src. as CPU or GPU addresses

## Slide 28: Summary of memory
CPU vs. GPU pointers
cudaMalloc()
cudaMemcpy()

## Slide 30: Part 2

## Slide 31: Recall…
GPUs…
  Have lots of cores
  Are suited toward “parallel problems”

## Slide 32: GPU internals

## Slide 33: GPU internals

## Slide 34: GPU internals

## Slide 35: CPU internals

## Slide 36: GPU internals
One instruction unit for multiple cores!

## Slide 37: Warps
Groups of threads simultaneously execute same instructions!
  Called a “warp”
  (32 threads in a warp under current standards)

## Slide 38: GPU internals

## Slide 39: Blocks
Group of threads scheduled to a multiprocessor
  Contain multiple warps
  Has a max. number (varies by GPU, e.g. 512 or 1024)

## Slide 40: Multiprocessor execution timeline

## Slide 41: Thread groups
A grid (all the threads started…):
  …contains blocks <- assigned to multiprocessors
    Each block contains warps <- executed simultaneously
      Each warp contains individual threads

## Slide 42: Part 2

## Slide 43
Moral 1: (from Lecture 1)
  Start lots of threads!
    Recall: Low context switch penalty
    Hide latency
  Start enough blocks!
    Occupy SMs
  e.g. Don’t call:
  kernel<<<1,1>>>(); // 1 block, 1 thread per block
  Call:
  kernel<<<50,512>>>();// 50 blocks, 512 threads per block

## Slide 44
Moral 2:
  Multiprocessors execute warps (of 32 threads)
    Block sizes of 32*n (integer n) are best
  e.g. Don’t call:
  kernel<<<50,97>>>(); // 50 blocks, 97 threads per block
  Call:
  kernel<<<50,128>>>();// 50 blocks, 128 threads per block

## Slide 45: Summary (processor internals)
Key parameters on kernel call:
  Threads per block
  Number of blocks
Choose carefully!

## Slide 47: Kernel argument passing
Similar to arg-passing in C functions
Some rules:
  Don’t pass host-memory pointers
  Small variables (e.g. individual ints) are fine
  No pass-by-reference

## Slide 48: Kernel function
Executed by many threads
Threads have unique ID mechanism:
  Thread index within block
  Block index

## Slide 49
Out of bounds issue:
  If index > (#elements), illegal access!

## Slide 50
Out of bounds issue:
  If index > (#elements), illegal access!

## Slide 51
#Threads issue:
  Cannot start e.g. 1e9 threads!
  Threads should handle arbitrary # of elements

## Slide 52
#Threads issue:
  Cannot start e.g. 1e9 threads!
  Threads should handle arbitrary # of elements

## Slide 53
#Threads issue:
  Cannot start e.g. 1e9 threads!
  Threads should handle arbitrary # of elements
Total number of blocks

## Slide 54
GPU -> CPU
Host memory pointer (copy to here)
Device memory pointer (copy from here)

## Slide 56
cudaFree()
  Equivalent to host memory’s free() function
  (As on host) Free memory after completion!

## Slide 57: Summary
GPU global memory:
  Pointers (CPU vs GPU)
  cudaMalloc() and cudaMemcpy()
GPU processor details:
  Thread group hierarchy
  Launch parameters
Threads in kernel