## Slide 1: CS 179: GPU Programming
Lecture 5: GPU Compute Architecture for the last time

## Slide 2: Last time...
GPU Memory System
  Different kinds of memory pools, caches, etc
  Different optimization techniques
Notes: I’ll mention shared memory a few more times in this lecture. shared memory is user programmable cache on SM.

## Slide 3: Warp Schedulers
Warp schedulers find a warp that is ready to execute its next instruction and available execution cores and then start execution
  GK110: 4 warp schedulers, 2 dispatchers in each SM
  Starts instructions in up to 4 warps each clock,
  and starts up to 2 instructions in each warp.
Notes: Each scheduler has 2 dispatchers.
Can start 2 instructions at once only if there are no instruction dependencies.
Note that it now takes up to 80 warp instructions to hide latency of warp add (10 cycles) rather than just 10 warp instructions.
GK110 has 15 SMs, so on a single clock up to 15 * 8 = 120 warp instructions initiated => 120 * 32 = 3840 scalar instructions.

## Slide 4: GK110 (Kepler) numbers
max threads / SM = 2048 (64 warps)
max threads / block = 1024 (32 warps)
32 bit registers / SM = 64k
max shared memory / SM = 48KB
The number of blocks that run concurrently on a SM depends on the resource requirements of the block!
Notes: ask what max threads / SM and max threads / block mean about how many blocks we need to achieve full occupancy

## Slide 5: Occupancy
occupancy = warps per SM / max warps per SM
max warps / SM depends only on GPU
warps / SM depends on warps / block, registers / block, shared memory / block.
Notes: We fit some integer number of blocks onto each SM.
threads/block matters because (combined with the number of blocks) let’s us know how many warps there are on the SM.
So what determines how many blocks are put on the SM?
register usage / block. You can specify __launch_bounds__ to limit register usage. Can easily get register usage numbers by setting a flag in nvcc.
shmem / block.
Could also consider “register occupancy” or “shared memory occupancy”, but I’ve never heard of anyone doing this.

## Slide 6: GK110 Occupancy
100% occupancy
2 blocks of 1024 threads
32 registers/thread
24KB of shared memory / block
50% occupancy
1 block of 1024 threads
64 registers/thread
48KB of shared memory / block
Notes: Higher occupancy is generally better, but certainly not always. Why might lower occupancy be better?
Lower occupancy allows hiding less latency, but there is also (hopefully) less latency to hide because each thread has more resources.
Share that for my GPU matrix multiplication implementation I found 25% occupancy works best (because 128 registers/thread)

## Slide 7: This lecture
  Synchronization
  Atomic Operations
  Instruction Dependencies
  Instruction Level Parallelism (ILP)

## Slide 8: Synchronization
Synchronization is a process by which multiple threads must indirectly communicate with each other in order to make sure they do not clash with each other
  Example of a synchronization issue:
    int x = 1;
    Thread 1 wants to add 1 to x;
    Thread 2 wants to add 1 to x;
    Thread 1 reads in the value of x (which is 1) into a register
    Thread 2 reads in the value of x (which is still 1) into a register
    Both threads increment the values they read in but they both think the final value is 2
    They write x back out and the final result is 2

## Slide 9: Synchronization
On a CPU, you can solve synchronization issues using Locks, Semaphores, Condition Variables, etc.
On a GPU, these solutions introduce too much memory and process overhead
  We have simpler solutions better suited for parallel programs

## Slide 10: CUDA Synchronization
Use the __syncthreads() function to sync threads within a block
  Only works at the block level
    SMs are separate from each other so can't do better than this
  Similar to barrier() function in C/C++

## Slide 11: Atomic Operations
Atomic Operations are operations that ONLY happen in sequence
  For example, if you want to add up N numbers by adding the numbers to a variable that starts in 0, you must add one number at a time
    Don't do this though. We'll talk about better ways to do this in the next lecture. Only use when you have no other options
CUDA provides built in atomic operations
  Use the functions: atomic<op>(float *address, float val);
    Replace <op> with one of: Add, Sub, Exch, Min, Max, Inc, Dec, And, Or, Xor
      e.g. atomicAdd(float *address, float val) for atomic addition
    These functions are all implemented using a function called atomicCAS(int *address, int compare, int val)
      CAS stands for compare and swap. The function compares *address to compare and swaps the value to val if the values are different

## Slide 12: Instruction Dependencies
acc += x[0];
acc += x[1];
acc += x[2];
acc += x[3];
...
An Instruction Dependency is a requirement relationship between instructions that force a sequential execution
  In the example on the right, each summation call must happen in sequence because the value of acc depends on the previous summation as well
Can be caused by direct dependencies or requirements set by the execution order of code
  I.e. You can't start an instruction until all previous operations have been completed in a single thread
Notes: Instruction dependencies are important to think about for high performance computing on x86, Nvidia architectures.
This is just an unrolled for loop.

## Slide 13: Instruction Level Parallelism (ILP)
Instruction Level Parallelism is when you avoid performances losses caused by instruction dependencies
  In CUDA, also removes performances losses caused by how certain operations are handled by the hardware

## Slide 14: ILP Example
z0 = x[0] + y[0];
z1 = x[1] + y[1];
x0 = x[0];
y0 = y[0];
z0 = x0 + y0;
x1 = x[1];
y1 = y[1];
z1 = x1 + y1;
COMPILATION
The second half of the code can't start execution until the first half completes
Notes: The x0 = x[0] lines indicate loading from memory into register, about 300 clocks.
Which instructions can overlap? Can we do better at overlapping instructions to hide latency?
HPC involves a lot of worrying about if the compiler is doing what you want.

## Slide 15: ILP Example
z0 = x[0] + y[0];
z1 = x[1] + y[1];
x0 = x[0];
y0 = y[0];
x1 = x[1];
y1 = y[1];
z0 = x0 + y0;
z1 = x1 + y1;
COMPILATION
Sequential nature of the code due to instruction dependency has been minimized.
Additionally, this code minimizes the number of memory transactions required
Notes: The x0 = x[0] lines indicate loading from memory into register, about 300 clocks.
Which instructions can overlap? Can we do better at overlapping instructions to hide latency?
HPC involves a lot of worrying about if the compiler is doing what you want.

## Slide 16: Questions?
  Synchronization
  Atomic Operations
  Instruction Dependencies
  Instruction Level Parallelism (ILP)

## Slide 17: Next time...
Set 2 Recitation on Friday (04/06)
GPU based algorithms (next week, lectures will be given by Aadyot)